## Slide 1: COMPUTER ARCHITECTURE LAB ONE
After graduating, you are asked to become the lead computer designer at Hyper Computers Inc. Your study of usage of high-level language constructs suggests that procedure calls are one of the most expensive operations. You have invented a scheme that reduces the loads and stores normally associated with procedure calls and returns. The first thing you do is run some experiments with and without this optimization. Your experiments use the same state-of-the-art optimizing compiler that will be used with either version of the computer. These experiments reveal the following information: The clock rate of the un optimized version is 5% higher. • 30% of the instructions in the un optimized version are loads or stores. • The optimized version executes 2/3 as many loads and stores as the un optimized version. For all other instructions the dynamic counts are unchanged. • All instructions (including load and store) take one clock cycle. Which is faster? Justify your decision quantitatively

## Slide 2
To determine which version of the computer is faster, we will compare the execution times for both versions.
Given data:
Clock rate of un optimized version = 1.05 × (clock rate of optimized version)
Percentage of load/store instructions in un optimized version = 30%
Reduction in load/store instructions in optimized version = ⅔ of the un optimized load/store instructions
All instructions take one clock cycle (CPI = 1 for all)
Other instruction counts remain unchanged.
Let:
IuI_u = Total number of instructions executed in the un optimized version.
IoI_o = Total number of instructions executed in the optimized version.
Since optimization only affects load/store instructions:
Load/store instructions in un optimized version = 0.30 × IuI_u
Load/store instructions in optimized version = (⅔) × (0.30 × IuI_u ) = 0.20 × IuI_u
Total instruction count in the optimized version:
Io=(Iu−0.30Iu)+0.20Iu=0.90IuI_o = (I_u - 0.30I_u) + 0.20I_u = 0.90I_u

## Slide 3
Execution time comparison
Execution time is given by:
Execution Time=Instruction Count × CPIClock Rate\text{Execution Time} = \frac{\text{Instruction Count} \times \text{CPI}}{\text{Clock Rate}}
Since CPI = 1 for both versions, execution time simplifies to:
Execution Time∝IClock Rate\text{Execution Time} \propto \frac{I}{\text{Clock Rate}}
Now, computing for both versions:
Unoptimized Execution Time:
Tu∝IufuT_u \propto \frac{I_u}{f_u}
Optimized Execution Time:
To∝0.90IufoT_o \propto \frac{0.90 I_u}{f_o}
Since fu=1.05fof_u = 1.05 f_o, we substitute:
To∝0.90Iufo=0.901.05TuT_o \propto \frac{0.90 I_u}{f_o} = \frac{0.90}{1.05} T_u To≈0.857TuT_o \approx 0.857 T_u

## Slide 4
Several researchers have suggested that adding a register-memory addressing mode to a load-store machine might be useful. The idea is to replace sequences of: LOAD Rx,0(Rb) ADD Ry, Ry, Rx by ADD Ry, 0(Rb) Assume this new instruction will cause the clock period of the CPU to increase by 5%. Use the instruction frequencies for the gec benchmark on the load-store machine from Table 1. The new instruction affects only the clock cycle and not the CPI.
What percentage of the loads must be eliminated for the machine with the new instruction to have at least the same performance?
Step 1: Define Execution Time Formula
Execution time is given by:
T=I×CPIfT = \frac{I \times \text{CPI}}{f}
Since the new instruction does not affect CPI, we simplify:
T∝IfT \propto \frac{I}{f}

## Slide 5
Step 2: Calculate Required Load Elimination Percentage
Let:
fof_o = Clock frequency of the original load-store machine.
fn=0.95fof_n = 0.95 f_o (since clock period increases by 5%).
IoI_o = Original instruction count.
pp = Fraction of loads eliminated.
Since loads are eliminated, total instruction count changes:
In=(1−p)IoI_n = (1 - p) I_o
For performance to remain the same:
Infn=Iofo\frac{I_n}{f_n} = \frac{I_o}{f_o}
Substituting values:
(1−p)Io0.95fo=Iofo\frac{(1 - p) I_o}{0.95 f_o} = \frac{I_o}{f_o}
Cancel IoI_o and solve for pp:
1−p=0.951 - p = 0.95 p=0.05p = 0.05
Thus, at least 5% of the loads must be eliminated for the performance to remain the same.

## Slide 6
2. Show a situation in a multiple instruction sequence where a load of a register (say Rx) followed immediately by a use of the same register (Rx) in an ADD instruction, could not be replaced by a single ADD instruction of the form proposed
The proposed ADD Ry, 0(Rb) replaces:
LOAD Rx, 0(Rb)
ADD Ry, Ry, Rx
However, this transformation fails in cases where Rx is used multiple times after being loaded. Consider:
LOAD Rx, 0(Rb)
ADD Ry, Ry, Rx
SUB Rz, Rx, Ra
If we replace only the LOAD + ADD with ADD Ry, 0(Rb), the subsequent SUB Rz, Rx, Ra would fail because Rx was never explicitly loaded into a register.
Thus, the register-memory ADD instruction is not always applicable when the loaded value is used more than once.

## Slide 7
In the early years of the RISC versus CISC dispute, the total number of different instructions and their variations in the ISA was a common indication of the "simplicity" of an ISA (lesser the number, greater the simplicity). Modern RISC instruction sets contain almost as many instructions as old CISC instruction sets. Discuss whether modern "RISC™ processors are no longer RISC (as envisioned in the 80's). If they are still RISC, then what features in the instruction set best define the simplicity of an ISA? (e.g. memory access instructions, fixed and simple instruction encoding, register-oriented instructions, simple data types, etc?)
Even though the Intel x86 ISA is a clear example of a CISC ISA, modern implementations of it (e.g. Core and Xeon) use many RISC ideas: register-based micro-instructions, pipelining. simple branch micro-instructions, fixed length micro-instructions, etc. Some say that, since at the low level the the latest Intel processors behave like a RISC, it is RISC. Others say that, since at the software interface (compiler) they are seen like a CISC, they are CISC. Discuss at what level we should measure the complexity of ISA? What are the implications of considering the ISA at each level? Are the latest Intel processors RISC?

## Slide 8
Are Modern "RISC" Processors Still RISC?
While modern RISC architectures include a large number of instructions, they still retain core RISC principles such as:
Load/Store Architecture: Memory access is restricted to specific load/store instructions, keeping arithmetic operations register-based.
Fixed and Simple Instruction Encoding: RISC architectures typically use fixed-length (e.g., 32-bit) instructions, making decoding simpler than CISC.
Regular Instruction Set with Few Addressing Modes: Unlike CISC, which supports complex addressing modes, RISC relies on simple, uniform instruction formats.
Register-Oriented Instructions: Operations occur between registers, minimizing memory access latency.

## Slide 9
However, modern RISC architectures (e.g., ARM, RISC-V) have added instructions for performance reasons, including SIMD, vector processing, and cryptographic operations. Despite this, their execution model remains RISC, as they prioritize simplicity in decoding, pipelining, and efficient instruction execution.
Is Intel x86 RISC or CISC?
Intel x86 processors internally operate more like RISC:
They translate complex CISC instructions into simpler micro-operations (µops) that resemble RISC instructions.
They use pipelining, fixed-length micro-instructions, and register renaming, all of which are RISC-like features.
However, at the software interface level, x86 remains CISC, because:
The ISA exposed to compilers includes variable-length instructions, multiple addressing modes, and complex instruction decoding.
Legacy support forces Intel to maintain CISC-like behavior externally.

## Slide 10
At What Level Should We Measure ISA Complexity?
Software Interface (Compiler View): If we consider the instruction set exposed to software, x86 is CISC, as compilers must handle its complexity.
Microarchitecture (Execution Engine View): If we analyze how instructions execute internally, x86 behaves like RISC, since instructions are broken into µops.
Implications of Considering Each Level:
Software-Level Complexity (CISC View):
  Compiler optimization is harder due to complex instructions.
  Maintaining backward compatibility limits simplifications.
Microarchitecture-Level Complexity (RISC View):
  Enables efficient pipelining, out-of-order execution, and better performance.
  Hardware design becomes more modular and scalable.