## Slide 1: BCT2408:COMPUTER ARCHITECTURE NAME:JUNE BOYANI REG NUMBER:SCT212-0067/2021
Fundamentals of Quantitative analysis and design

## Slide 2: 1.1 INTRODUCTION
Computer technology has made incredible progress in the roughly 65 years since the first general-purpose electronic computer was created this rapid improvement has come both from advances in the technology used to build computers and from innovations in computer design.
Although technological improvements have been fairly steady, progress arising from better computer architectures has been much less consistent. The late 1970s saw the emergence of the microprocessor. The ability of the microprocessor to ride the improvements in integrated circuit technology led to a higher rate of performance improvement—roughly 35% growth per year.
This growth rate, combined with the cost advantages of a mass-produced microprocessor, led to an increasing fraction of the computer business being based on microprocessors. In addition, two significant changes in the computer marketplace made it easier than ever before to succeed commercially with a new architecture.
These changes made it possible to develop successfully a new set of architectures with simpler instructions, called RISC (Reduced Instruction Set Computer) architectures, in the early 1980s.

## Slide 3
Second, this dramatic improvement in cost-performance leads to new classes of computers. Personal computers and workstations emerged in the 1980s with the availability of the microprocessor. The last decade saw the rise of smart cell phones and tablet computers, which many people are using as their primary computing platforms instead of PCs.
Third, continuing improvement of semiconductor manufacturing as predicted by Moore’s law has led to the dominance of microprocessor-based computers across the entire range of computer design. Minicomputers, which were traditionally made from off-the-shelf logic or from gate arrays, were replaced by servers made using microprocessors.
This hardware renaissance led to the fourth impact, which is on software development. The nature of applications also changes. Speech, sound, images, and video are becoming increasingly important, along with predictable response time that is so critical to the user experience.

## Slide 4: 1.2 CLASSES OF COMPUTERS
Personal mobile device (PMD) is the term we apply to a collection of wireless devices with multimedia user interfaces such as cell phones, tablet computers, and so on. Applications on PMDs are often Web-based and media-oriented, like the Google Goggles example above.
Desktop Computing the first, and probably still the largest market in dollar terms, is desktop computing. Desktop computing spans from low-end netbooks that sell for under $300 to high-end, heavily configured workstations that may sell for $2500.
Servers as the shift to desktop computing occurred in the 1980s, the role of servers grew to provide larger-scale and more reliable file and computing services. Such servers have become the backbone of large-scale enterprise computing, replacing the traditional mainframe.

## Slide 5
Embedded Computers ;embedded computers are found in everyday machines; microwaves, washing machines, most printers, most networking switches, and all cars contain simple embedded microprocessors. The processors in a PMD are often considered embedded computers, but we are keeping them as a separate category because PMDs are platforms that can run externally developed software and they share many of the characteristics of desktop computers. Other embedded devices are more limited in hardware and software sophistication.
CLASSES OF PARALLELISM AND PARALLEL ARCHITECTURES
There are basically two kinds of parallelism in applications:
1. Data-Level Parallelism (DLP) arises because there are many data items that can be operated on at the same time.
2. Task-Level Parallelism (TLP) arises because tasks of work are created that can operate independently and largely in parallel.
Computer hardware in turn can exploit these two kinds of application parallelism in four major ways:
Instruction-Level Parallelism exploits data-level parallelism at modest levels with compiler help using ideas like pipelining and at medium levels using ideas like speculative execution.
2. Vector Architectures and Graphic Processor Units (GPUs) exploit data-level parallelism by applying a single instruction to a collection of data in parallel.
3.

## Slide 6
3. Thread-Level Parallelism exploits either data-level parallelism or task-level
parallelism in a tightly coupled hardware model that allows for interaction
among parallel threads.
4. Request-Level Parallelism exploits parallelism among largely decoupled tasks specified by the programmer or the operating system.
Michael flynn looked at the parallelism in the instruction and data streams called for by the instructions at the most constrained component of the multiprocessor, and placed all computers into one of four categories:
1. Single instruction stream, single data stream (SISD)—This category is the uniprocessor. The programmer thinks of it as the standard sequential computer, but it can exploit instruction-level parallelism. Chapter 3 covers SISD architectures that use ILP techniques such as superscalar and speculative execution.
2. Single instruction stream, multiple data streams (SIMD)—The same instruction is executed by multiple processors using different data streams. SIMD computers exploit data-level parallelism by applying the same operations to multiple items of data in parallel. Each processor has its own data memory (hence the MD of SIMD), but there is a single instruction memory and control processor, which fetches and dispatches instructions. Chapter 4 covers DLP and three different architectures that exploit it: vector architectures, multimedia extensions to standard instruction sets, and GPUs.
3. Multiple instruction streams, single data stream (MISD)—No commercial multiprocessor of this type has been built to date, but it rounds out this simple classification.
4. Multiple instruction streams, multiple data streams (MIMD)—Each processor fetches its own instructions and operates on its own data, and it targets task-level parallelism. In general, MIMD is more flexible than SIMD and thus more generally applicable, but it is inherently more expensive than SIMD. For example, MIMD computers can also exploit data-level parallelism, although the overhead is likely to be higher than would be seen in an SIMD computer.

## Slide 7: 1.3 DEFINING COMPUTER ARCHITECTURE
The task the computer designer faces is a complex one: Determine what
attributes are important for a new computer, then design a computer to maximize
performance and energy efficiency while staying within cost, power, and availability constraints. This task has many aspects, including instruction set design, functional organization, logic design, and implementation. The implementation may encompass integrated circuit design, packaging, power, and cooling.
Instruction Set Architecture: The Myopic View of Computer Architecture
We use the term instruction set architecture (ISA) to refer to the actual programmer
visible instruction set in this book. The ISA serves as the boundary between the software and hardware.

## Slide 8
This quick review of ISA will use examples from 80x86, ARM, and MIPS to illustrate the seven dimensions of an ISA;
1.Class of ISA—Nearly all ISAs today are classified as general-purpose register architectures, where the operands are either registers or memory locations.
2. Memory addressing—Virtually all desktop and server computers, including the 80x86, ARM, and MIPS, use byte addressing to access memory operands.
3. Addressing modes—In addition to specifying registers and constant operands, addressing modes specify the address of a memory object.
4. Types and sizes of operands—Like most ISAs, 80x86, ARM, and MIPS support operand sizes of 8-bit (ASCII character), 16-bit (Unicode character or half word), 32-bit (integer or word), 64-bit (double word or long integer), and IEEE 754 floating point in 32-bit (single precision) and 64-bit (double precision). The 80x86 also supports 80-bit floating point (extended double precision).
5. Operations—The general categories of operations are data transfer, arithmetic logical, control (discussed next), and floating point. MIPS is a simple and easy-to-pipeline instruction set architecture, and it is representative of the RISC architectures being used in 2011.

## Slide 9
6.Control flow instructions—Virtually all ISAs, including these three, support
conditional branches, unconditional jumps, procedure calls, and returns. All
three use PC-relative addressing, where the branch address is specified by an
address field that is added to the PC.
7. Encoding an ISA—There are two basic choices on encoding: fixed length and
variable length. All ARM and MIPS instructions are 32 bits long, which simplifies instruction decoding.
Genuine Computer Architecture: Designing the Organization and Hardware to Meet Goals and Functional Requirements
The implementation of a computer has two components: organization and hardware. The term organization includes the high-level aspects of a computer’s design, such as the memory system, the memory interconnect, and the design of the internal processor or CPU (central processing unit—where arithmetic, logic, branching, and data transfer are implemented). The term microarchitecture is also used instead of organization. Hardware refers to the specifics of a computer, including the detailed logic design and the packaging technology of the computer.

## Slide 10: 1.4 TRENDS IN TECHNOLOGY
If an instruction set architecture is to be successful, it must be designed to survive rapid changes in computer technology. After all, a successful new instruction set architecture may last decades—for example, the core of the IBM mainframe has been in use for nearly 50 years.
To plan for the evolution of a computer, the designer must be aware of rapid
changes in implementation technology. Five implementation technologies, which
change at a dramatic pace, are critical to modern implementations:
Integrated circuit logic technology—Transistor density increases by about 35% per year, quadrupling somewhat over four years.
Semiconductor DRAM (dynamic random-access memory)—Now that most DRAM chips are primarily shipped in DIMM modules, it is harder to track chip capacity, as DRAM manufacturers typically offer several capacity products at the same time to match DIMM capacity

## Slide 11
Semiconductor Flash (electrically erasable programmable read-only memory)—This nonvolatile semiconductor memory is the standard storage device in PMDs, and its rapidly increasing popularity has fueled its rapid growth rate in capacity.
Magnetic disk technology—Prior to 1990, density increased by about 30% per year, doubling in three years. It rose to 60% per year thereafter, and increased to 100% per year in 1996. Since 2004, it has dropped back to about 40% per year, or doubled every three years. Disks are 15 to 25 times cheaper per bit than Flash.
Network technology—Network performance depends both on the performance of switches and on the performance of the transmission system.

## Slide 12
Performance Trends: Bandwidth over Latency
Bandwidth or throughput is the total amount of work done in a given time, such as megabytes per second for a disk transfer. In contrast, latency or response time is the time between the start and the completion of an event, such as milliseconds for a disk access.
Scaling of Transistor Performance and Wires
Integrated circuit processes are characterized by the feature size, which is the
minimum size of a transistor or a wire in either the x or y dimension. Feature
sizes have decreased from 10 microns in 1971 to 0.032 microns in 2011; in fact,
we have switched units, so production in 2011 is referred to as “32 nanometers,”
and 22 nanometer chips are under way.

## Slide 13: 1.5 TRENDS IN POWER AND ENERGY IN INTERGRATED CIRCUITS
Today, power is the biggest challenge facing the computer designer for nearly every class of computer. First, power must be brought in and distributed around the chip, and modern microprocessors use hundreds of pins and multiple interconnect layers just for power and ground. Second, power is dissipated as heat and must be removed.
Power and Energy: A Systems Perspective
How should a system architect or a user think about performance, power, and energy? From the viewpoint of a system designer, there are three primary concerns:
First, what is the maximum power a processor ever requires? Meeting this demand can be important to ensuring correct operation. For example, if a processor attempts to draw more power than a power supply system can provide (by drawing more current than the system can supply), the result is typically a voltage drop, which can cause the device to malfunction.

## Slide 14
Second, what is the sustained power consumption? This metric is widely called the thermal design power (TDP), since it determines the cooling requirement. TDP is neither peak power, which is often 1.5 times higher, nor is it the actual average power that will be consumed during a given computation, which is likely to be lower still. A typical power supply for a system is usually sized to exceed the TDP, and a cooling system is usually designed to match or exceed TDP. Failure to provide adequate cooling will allow the junction temperature in the processor to exceed its maximum value, resulting in device failure and possibly permanent damage.
The third factor that designers and users need to consider is energy and energy efficiency. Recall that power is simply energy per unit time: 1 watt = 1 joule per second. Which metric is the right one for comparing processors: energy or power? In general, energy is always a better metric because it is tied to a specific task and the time required for that task.

## Slide 15
Energy and Power within a Microprocessor
For CMOS chips, the traditional primary energy consumption has been in switching transistors, also called dynamic energy. The energy required per transistor is proportional to the product of the capacitive load driven by the transistor and the square of the voltage.
The capacitive load is a function of the number of transistors connected to an output
and the technology, which determines the capacitance of the wires and the transistors.
Distributing the power, removing the heat, and preventing hot spots have become increasingly difficult challenges. Power is now the major constraint to using transistors; in the past, it was raw silicon area. Hence, modern microprocessors offer many techniques to try to improve energy efficiency despite flat clock rates and constant supply voltages:
1. Do nothing well. Most microprocessors today turn off the clock of inactive modules to save energy and dynamic power. For example, if no floating-point instructions are executing, the clock of the floating-point unit is disabled. If some cores are idle, their clocks are stopped.
2. Dynamic Voltage-Frequency Scaling (DVFS). The second technique comes directly from the formulas above. Personal mobile devices, laptops, and even servers have periods of low activity where there is no need to operate at the highest clock frequency and voltages.

## Slide 16
3. Design for typical case. Given that PMDs and laptops are often idle, memory and storage offer low power modes to save energy.
4. Overclocking. Intel started offering Turbo mode in 2008, where the chip
decides that it is safe to run at a higher clock rate for a short time possibly on
just a few cores until temperature starts to rise.

## Slide 17: 1.6 TRENDS IN COST
Although costs tend to be less important in some computer designs—specifically supercomputers—cost-sensitive designs are of growing significance. Indeed, in the past 30 years, the use of technology improvements to lower cost, as well as increase performance, has been a major theme in the computer industry.
The Impact of Time, Volume, and Commoditization
The cost of a manufactured computer component decreases over time even without major improvements in the basic implementation technology. The underlying principle that drives costs down is the learning curve—manufacturing costs decrease over time. The learning curve itself is best measured by change in yield—the percentage of manufactured devices that survives the testing procedure. Whether it is a chip, a board, or a system, designs that have twice the yield will have half the cost. Understanding how the learning curve improves yield is critical to projecting costs over a product’s life.

## Slide 18
Cost of an Integrated Circuit
Cost of integrated circuit = Cost of die + Cost of testing die + Cost of packaging and final test /Final test yield
Learning how to predict the number of good chips per wafer requires first
learning how many dies fit on a wafer and then learning how to predict the percentage of those that will work. From there it is simple to predict cost:
Cost of die=cost of wafer/dies per wafer*die yield
Dies per wafer =π ( ) Wafer diameter/2
2
×
Die area
----------------------------------------------------------
-
= –
π
× Wafer diameter
2 Die are

## Slide 19
Die yield Wafer yield 1 1 Defects per unit area Die area ⁄ ( ) + × N
Cost versus Price
With the commoditization of computers, the margin between the cost to manufacture a product and the price the product sells for has been shrinking. Those1.7 Dependability 33 margins pay for a company’s research and development (R&D), marketing, sales, manufacturing equipment maintenance, building rental, cost of financing, pretax profits, and taxes.
Cost of Manufacturing versus Cost of Operation
For the first four editions of this book, cost meant the cost to build a computer and price meant price to purchase a computer. With the advent of warehouse scale computers, which contain tens of thousands of servers, the cost to operate the computers is significant in addition to the cost of purchase.
Thus, to lower operational costs in a warehouse-scale computer, computer architects need to use energy efficiently.